## Slide 1: EE4321 Digital Systems Design using HDL
Final Project
Mark W. Welker

## Slide 2: Project: Simplistic Matrix engine
You will be creating the basic matrix unit that could be utilized in deep learning.
The matrix unit will perform matrix multiplication, scaler multiplication, subtraction, addition, and transposition.
A testbench will place a starting set of matrix in RAM. It will also place the opcodes for the execution unit to perform the matrix functions using the matrix modules.

## Slide 3: Project Details
All math functions will have a clear input to set it to 0.
The Register value needs to be able to be written back into a memory location
All Matrices will be 4x4 16 bit deep.
Matrix multiplier will multiple two 4x4 matrix and return a 4x4 matrix
Scalar multiplication is multiplying a matrix by a single number
Add and Subtract will add and subtract 2 4x4 matrix
Transpose will flip a matrix along its diagonal.
If you want to brush up an Matrix Math
  https://www.mathsisfun.com/algebra/matrix-introduction.html

## Slide 4: Project: Test Bench operation
Load 2 matrix’s into RAM
Load opcodes into RAM for the execution unit.
Operations to be performed
Add the first matrix to the second matrix and store the result.
Transpose the result from step 1 store in memory
Subtract the second matrix from the result in step 2 and store the result somewhere else in memory.
Scale the result in step 3
Multiply the result from step 4 by the result in step 3, store in memory.

## Slide 5: Project: Matrix MATH function and Accumulator
Matrix Modules
RAM
Adder / Subtractor
Scalar Multiplication
Multiply
Transpose
Register
Execution Unit

## Slide 6: Project Details
The test bench will place the starting matrixes in memory and toggle reset
Execution engine will fetch the first opcode from memory and begin execution.
The execution engine will direct the transfer of data between the memory, the appropriate matrix modules and memory.
The execution engine will continue executing programs until is finds a STOP opcode.
The test bench will instantiate ALL models and create an output waveform to determine correct operation. The test bench will ALSO provide the system clock as well as the number of clock cycles required to complete the tasks.

## Slide 7: Project Recommendations
Execution engine
  You will need to generate your own opcode set it should include opcodes for
    STOP
    Matrix Addition to/from memory, to/from register
    Matrix Subtraction to/from memory, to/from register
    Matrix Multiply to/from memory, to/from register
    Matrix Transpose to/from memory, to/from register
    Matrix scale to/from memory, to/from register
  You are free to designate the opcodes any way you wish
Registers can be implemented as a register file or as a registers in the modules.
You will need to determine how you wish to transfer the matrix between modules.